## Slide 1
A multi-time-scale wall model for Large Eddy Simulation of non-equilibrium flows
Presenter: Mitchell Fowler
Advisors: Charles Meneveau, Tamer Zaki
Monday, November 13, 2023
Research supported by ONR
Dissertation Defense
Notes: Thank you Charles/Tamer for the introduction. I’m excited to introduce the research I have been working on over the course of my PhD. In particular I will be discussing a multi-time-scale wall model for Large Eddy Simulation of non-equilibrium flows.

## Slide 2: Outline
Introduction
The Lagrangian Relaxation Towards Equilibrium (LaRTE) model
The laminar non-equilibrium (lamNEQ) model
Applications of the LaRTE+lamNEQ wall model to equilibrium and non-equilibrium channel flows
The multi-time-scale wall model (MTSWM)
The MTSWM applied to horizontally homogeneous flows
The MTSWM applied to streamwise developing flows
Summary, conclusions, and future directions
Acknowledgements
Chapter
Chapter
Chapter
Chapter
Chapter
Chapter
Chapter
Chapter
Notes: The outline follows my dissertation. First I’ll provide an introduction with background information and motivation for my work. Then I’ll discuss the theory behind the LaRTE and lamNEQ models and their application to equilibrium and non-equilibrium channel flows. Then I’ll introduce the full multi-time-scale wall model which includes an additional turbulent non-equilibrium model. I’ll then apply with wall model to channel and streamwise developing flows. Then I’ll finish with conclusions, future directions and acknowledgments.

## Slide 3: Chapter 1 – Introduction

## Slide 4: Large Eddy Simulation (LES): a high fidelity tool for engineering applications
Wall resolved LES of a 6:1 prolate spheroid
Plasseraud, Kumar, & Mahesh (2023, JFM)
Isosurfaces of Q-criterion colored by the velocity magnitude
Wall modeled LES of an aircraft
Skin friction (gray contours on surface)
And axial velocity (colored contours on transverse planes)
Right: Goc, Lehmkuhl, Park, Bose, & Moin (2021, Flow)
Left: Lozano-Durán, Bose, & Moin (2022, AIAA)
Notes: First, what is Large Eddy Simulation? Large eddy simulation is a type of simulation where large scales of the flow are resolved and smaller, more universal scales are model. The result is a high fidelity simulation which can accurately capture complex dynamics not possible by lower fidelity simulations like RANS. You can see examples of this through the pictures shown here which include a wall modeled LES of an entire aircraft and wall resolved LES of a prolate spheroid, similar to a submarine. These types of simulations have only recently been possible, largely due to advances in modeling such as wall models.

## Slide 5: Background/Motivation
Unsteady flows are everywhere
Change in direction
of mean flow
Sudden spanwise
pressure gradient
Change in magnitude of mean flow
Pulsatile pipe flow
Accelerating/decelerating
channel flow
Statistically stationary
turbulent flow
Real world
example
Test case
example
Any steady,
turbulent flow
Notes: The primary application and motivation for this work is unsteady flows. Here you can see there are a variety of examples of where unsteadiness occurs which can be categorized as changes in direction and magnitude of mean flow like the three images on the left, and even statistically stationary turbulent flow inherently has unsteadiness.

## Slide 6: Background/Motivation
Wall Resolved LES
Near wall grid
refinement
Wall Modeled LES
Near wall effects
modelled
Choi & Moin (2012)
Physics of Fluids, 24(1), 011702
grid point requirements for a
turbulent boundary layer
Nearly reduction in number of points required
Notes: On the left you can see what a typical mesh looks like for wall resolved LES where there is near-wall grid refinement. And on the right you can see a wall modeled LES mesh where no near-wall grid refinement is needed because this inner layer is modeled. The result is simulation cost savings. Choi and moin showed that wall modeled LES achieves a Reynolds number reduction in the number of grid points required compared to wall resolved LES.

## Slide 7: Background/Motivation
Wall modeled LES
unresolved
near-wall
dynamics
Goal: find wall-stress, , given LES inputs (e.g. or )
wall-modeling height
Notes: The goal of a wall model is to compute the wall stress given LES inputs (such as the velocity and pressure gradient) at the wall model height, \Delta. This is difficult because there are many complex, near-wall dynamics not resolved by the LES that affect the wall stress.

## Slide 8: Equilibrium wall model (EQWM)
time scales
LES
Wall modeling region
Log layer
Equilibrium model closure for with as input
Stresses assumed to be in equilibrium
wall
(iteratively solve for )
or
where is fitted (Meneveau 2020, JoT)
Notes: The most common and popular wall model is the equilibrium wall model. Called such because it assumes stresses are in equilibrium, or in other words the wall stress is set equal to the total stress at the wall model height. Then the wall stress is connected to the LES velocity by assuming some sort of velocity profile profile form such as the log-law where the wall stress must be solved for using an iterative method. Meneveau in 2020 developed several different fitting functions to avoid iteration which we use here.

## Slide 9: Flows where the EQWM fails
Stationary channel flow
DNS (JHTDB)
Instantaneous velocity profiles do not collapse!
Sudden spanwise pressure gradient
EQWM
DNS
Laminar
Solution
DNS from Lozano-Duran et al. 2020, JFM
EQWM
DNS
Laminar solution
DNS from Jung & Kim 2017,
Int. J. Heat Fluid Flow
Linearly accelerating
channel flow
The EQWM fails in a variety of situations.
It appears advantageous to separate equilibrium and non-equilibrium wall stress contributions!
Notes: Despite its popular usage, the equilibrium wall model fails in a variety of situations.

## Slide 10: Chapter 2 – The Lagrangian Relaxation Towards Equilibrium (LaRTE) model

## Slide 11: The Lagrangian relaxation towards equilibrium (LaRTE) wall model
Model intended to capture quasi-equilibrium dynamics
Main ansatz: velocity satisfies the law of the wall
Goal: develop evolution equation for
  Wall stress:
where
Velocity profile produced using LES simulation data
Notes: The friction slowly varies in time and space.
For picture: velocity profile is assumed to satisfy law of the wall below the wall modeling height y = Delta
Below you can a schematic and animation demonstrating the usefulness of this approach. The LES velocity, at our wall model height, Delta, is provided as an input to the wall model. This velocity fluctuates significantly but what we have found is that by assuming the inner layer satisfies the law of the wall we can extract the slower, quasi-equilibrium dynamics.

## Slide 12: The LaRTE model derivation
Substitute law of the wall velocity profile into RANS eq., , use continuity, and simplify*
where
“important terms”
Equilibrium stress closure:
*This is a wall-parallel plane 2D PDE at LES-resolution, i.e. very small additional cost.
Notes: We can describe the friction velocity as a Lagrangian relaxation towards its equilibrium value

## Slide 13: LaRTE wall model
Simplified form for x-component
where
relaxes (in a Lagrangian sense) towards
(the equilibrium value)
at the relaxation time scale
Inertial fluid
layer
EQWM
LaRTE
Real simulation results
For true equilibrium (the limit ):
For quasi-equilibrium:

## Slide 14: LaRTE a priori test
DNS velocity data from JHTDB filtered at various time scales
  Is consistent with quasi-equilibrium?
Collapse = quasi-equilibrium
No filter
Global normalization
(constant in time)
Local normalization
(time dependent)

## Slide 15: LaRTE length and time scale schematic
Quasi-equilibrium (LaRTE)
relaxation
time scales
LES
Wall modeling region
Log layer
Equilibrium model closure for
(relaxation time scale, slow)

## Slide 16: Chapter 3 – the laminar non-equilibrium (lamNEQ) model

## Slide 17: The laminar non-equilibrium (lamNEQ) model
Model equation for “laminar non-equilibrium velocity”
Wall stress analytical solution
High frequency content
of the LES PG:
Velocity response to PG:
Laminar viscous sublayer

## Slide 18: The laminar non-equilibrium (lamNEQ) model
Efficient evaluation is possible through a sum-of-exponentials (SOE) approximation to the kernel, Jiang et al. 2017
Allows convolution integral to be computed recursively
(where and are constants computed a-priori)
Pressure gradient input
Wall stress output
Dashed Lines – L1 Method (“truth”)
Solid Lines – SOE approx.

## Slide 19: Chapter 4 – Applications of the LaRTE+lamNEQ wall model to equilibrium and non-equilibrium channel flows

## Slide 20: LaRTE + lamNEQ length and time scales
Quasi-equilibrium (LaRTE)
relaxation
time scales
LES
Wall modeling region
Log layer
Equilibrium model closure for
(viscous time scale, fast)
(relaxation time scale, slow)
Viscous
sublayer
Laminar
Stokes
layer

## Slide 21: A posteriori tests
LaRTE
lamNEQ
19
Total wall stress is applied as the boundary condition to the LES
Statistically stationary channel flow
Code: LESGO
Lagrangian scale dependent SGS model
1st grid point used for wall model height

## Slide 22: Test simulations – statistically stationary channel flow
Statistics
Time signals
Lagrangian vs Eulerian relaxation
EQWM
LaRTE
LaRTE
lamNEQ
DNS
LES
Lagrangian
Eulerian
(same initial condition coming from the Lagrangian simulation)

## Slide 23: A posteriori tests
LaRTE
lamNEQ
19
Total wall stress is applied as the boundary condition to the LES
Channel flow with sudden spanwise pressure gradient (SSPG)
Code: LESGO
Lagrangian scale dependent SGS model
1st grid point used for wall model height

## Slide 24: Test simulations – sudden spanwise pressure gradient
Large spanwise pressure gradient () applied for
Wall stress response
Wall stress contour animation
DNS
LES
LaRTE
lamNEQ

## Slide 25: Chapter 5 – The multi-time-scale wall model (MTSWM)

## Slide 26: LaRTE+lamNEQ wall stress probability density functions
LaRTE
lamNEQ
DNS
LES
Streamwise wall stress fluctuations underpredicted!

## Slide 27: LaRTE + lamNEQ length and time scales
Quasi-equilibrium (LaRTE)
relaxation
time scales
LES
Wall modeling region
Log layer
Equilibrium model closure for
(viscous time scale, fast)
(relaxation time scale, slow)
Viscous
sublayer
Laminar
Stokes
layer
Missing physics to be modeled!

## Slide 28: Turbulent non-equilibrium (turbNEQ) model
Turbulent velocity fluctuation
Low momentum streak
High momentum streak
High momentum streak
for
for
Wall attached
eddies
Velocity profile agrees
with POD mode shown in
Hansen et. al 2022,
(CTR Summer Program 2022)

## Slide 29: Multi-time-scale (MTS) wall model
time scales
Equilibrium model closure for
Quasi-equilibrium (LaRTE)
LES
Wall modeling region
Viscous
sublayer
Log layer
Turbulent
non-
equilibrium
relaxation
Laminar
Stokes
layer
(viscous time scale, fast)
(relaxation time scale, slow)

## Slide 30: Chapter 6 – The MTSWM applied to horizontally homogeneous flows
Notes: Flows focus on temporal non-equilibrium

## Slide 31: Revising wall stress probability density functions with MTSWM
LaRTE
lamNEQ
DNS
LES
Streamwise wall stress fluctuations match DNS!
turbNEQ
Overpredicts spanwise variance

## Slide 32: The MTSWM applied to non-equilibrium flows
Pulsatile channel flow
Primary DNS reference: Weng et al. (2016)
PG forcing:
MTS wall stress BC
Non-equilibrium parameter: frequency
Total = LaRTE + turbNEQ + lamNEQ

## Slide 33: JFM Notebooks
Fowler, Zaki, Meneveau (2023), JFM,
DOI: https://doi.org/10.1017/jfm.2023.585
Notes: First, as a bit of a shameless plug, the results for this chapter were recently published in a paper which uses JFM notebooks.

## Slide 34: Pulsatile channel flow
DNS
MTSWM
EQWM
Wall stress
Wall stress
02

## Slide 35: Pulsatile channel flow
DNS
MTSWM
Wall stress
Wall stress
02
LaRTE
lamNEQ
turbNEQ
LaRTE
turbNEQ
lamNEQ
Quasi-steady
Intermediate frequency
High frequency

## Slide 36: The MTSWM applied to non-equilibrium flows
Laminar stage
Transition stage
Final turbulent state
Linearly accelerating channel flow
DNS reference: Jung & Kim (2017)
PG forcing:
From Jung & Kim (2017)
Non-equilibrium parameter: “acceleration/ramp rate”
time
(initial turbulent state)
(final turbulent state)

## Slide 37: Linearly accelerating channel flow
DNS
MTSWM
EQWM
Laminar solution
Laminar stage
Transition stage
Final turbulent state

## Slide 38: Linearly accelerating channel flow
DNS
MTSWM
LaRTE
turbNEQ
lamNEQ
LaRTE
lamNEQ
turbNEQ

## Slide 39: Chapter 7 – The MTSWM applied to streamwise developing flows
Notes: Previous tests have focused on temporal non-equilibrium. Now we want to test spatial non-equilibrium.

## Slide 40: LESGO code development
Fringe Body Force
computed using modified rescale-recycle method based on Lund et al. (1998)

## Slide 41: Zero pressure gradient (ZPG) turbulent boundary layers over a wide range of Reynolds numbers
Based on WMLES of Inoue and Pullin (2011)
prescribed using modified rescale-recycle method
Code: LESGO
Lagrangian scale dependent SGS model
1st grid point used for wall model height

## Slide 42: ZPG statistics over a wide range of Re
Empirical Fit
MTSWM
EQWM
MTSWM
EQWM
Turbulence intensities collapse
LES agrees with empirical trends

## Slide 43: ZPG statistics over a wide range of Re
Empirical Fit
MTSWM
EQWM
Empirical Fit
Skin friction falls within 10% of expectation

## Slide 44: Separation bubble induced by suction and blowing boundary condition
Suction
Blowing
Based on DNS of Coleman et al. (2018)
ZPG1
ZPG2
prescribed

## Slide 45: Separated flow simulation results
DNS
MTSWM
EQWM

## Slide 46: Separated flow simulation results
DNS
MTSWM
EQWM

## Slide 47: Separated flow simulation results
DNS
MTSWM
EQWM
LES does not show mean flow separation

## Slide 48: Separated flow simulation results
DNS
MTSWM
EQWM
= fraction of reversed wall stress (fraction of time )

## Slide 49: Separated flow simulation results
DNS
MTSWM
EQWM
= fraction of reversed wall stress (fraction of time )
MTSWM more realistically predicts wider than EQWM

## Slide 50: Separated flow simulation results
Total
LaRTE
lamNEQ
turbNEQ

## Slide 51: Separated flow simulation results – MTSWM PDFs
Total
LaRTE
lamNEQ
turbNEQ

## Slide 52: Chapter 8 – Summary, conclusions, and future directions

## Slide 53: Summary and conclusions
Developed a multi-time-scale wall model for non-equilibrium LES
  LaRTE – captures slow, quasi-equilibrium wall stress behavior
  lamNEQ – captures wall stress response to fast changes in PG affecting laminar Stokes layer dynamics
  turbNEQ – captures wall stress response to velocity fluctuations characteristic of turbulent eddies
Tested MTSWM for a wide range of flow conditions from quasi-equilibrium to non-equilibrium and compared against EQWM and available DNS
  Includes stationary channel flows, channel flow with SSPG, pulsatiling channel flow, linearly accelerating channel flow, ZPG developing boundary layer, and a separated boundary layer
  MTSWM clearly outperforms EQWM during high non-equilibrium conditions (high frequency / fast acceleration)
  Pulsating & Linearly accelerating flows show usefulness of the MTSWM approach
    Different components capure different time scale dynamics
  LES for ZPG boundary layer and separated flow tests show good agreement with DNS
    MTSWM more realistically predicts wider than EQWM

## Slide 54: Future directions & publications
Expand application cases
  Flows with larger separation
  Combined temporal and spatial non-equilibrium
  Complex geometry
Continue improving models
  Extend to rough walls
  Improve spanwise PDFs
  Develop alternate turbNEQ models
Code improvement
  Fringe region generates large PG at inlet
  Improve performance in fringe region
Fowler, Zaki, Meneveau (2022), JFM,
DOI: https://doi.org/10.1017/jfm.2021.1156
Fowler, Zaki, Meneveau (2023), JFM,
DOI: https://doi.org/10.1017/jfm.2023.585
Additional details can be found in: